## Slide 1: CSCI 558L Lecture 10: Programmable Network Cards
Internetworking and Distributed Systems Laboratory
Young Cho
Department of Computer Science
University of Southern California

## Slide 2: Programmable Network Interface
Network Processor
Fast Memory for Network
Flexible Design
As Opposed to Traditional NIC
  In essence PHY only
  Leverages mainboard processor/memory
Memory
BUS
PHY
Network
Processor
Network

## Slide 3: Programmable Network Interface
Software Programmable NICs
  Intel IQ960-RD66 Evaluation Card
  Cyclone Microsystems
    http://www.cyclone.com/products/network_adapters/index.php
  Quadrics
  Myrinet
    http://www.myri.com
Hardware/Software Programmable NICs
  RiceNIC
    http://www.cs.rice.edu/CS/Architecture/ricenic/
  NetFPGA
    http://www.netfpga.org
  Other FPGA based NICs

## Slide 4: Network Processor
Terminology emerged in the industry 1997-1998
  Many startups competing for the network building-block
  Broad variety of products are presented as an NP
Function
  Integration and programmability
  Efficient processing of network headers in packets
  Support for higher-level flow management
Wide spectrum of capabilities and target markets

## Slide 5: Motivation
“Flexibility of a fully programmable processor with performance approaching that of a custom ASIC.”
  Faster time to market (no ASIC lead time)
  Instead you get software development time
Field upgradability leading to longer lifetime
  Ability to adapt deployed equipment to evolving and emerging standards and new application spaces
  Enables multiple products using common hardware
Allows the network equipment vendors to focus on their value-add

## Slide 6: Usage
Integrated GPP + system controller + “acceleration”
Fast forwarding engine with access to a “slow-path” control agent
A smart DMA engine
An intelligent NIC
A highly integrated set of components to replace a bunch of ASICs and the blade control uP

## Slide 7: Features
Integrated or attached GPP
Pool of multithreaded forwarding engines
High Bandwidth and High Capacity Mems
  Embedded and external SRAM and DRAM
Variety of Communication mediums
  Integrated media interface or media bus
  Interface to a switching fabric or backplane
  Interface to a “host” control processor
  Interface to coprocessors

## Slide 8: Advantages
Higher Performance
  Specialized network processing engines
  Multiple processing elements
  Low Latency
Intelligence
  Network level without going to main processor
Modularity
  Taking the processing load off GPP
  NP handles the network
  GPP handles the application

## Slide 9: NP Architectural Challenges
Application-specific architecture
  Yet, covering a very broad space with varied (and ill-defined) requirements and no useful benchmarks
  Need to understand the environment
  Need to understand network protocols
  Need to understand networking applications
Have to provide solutions before the actual problem is defined
  Decompose into the things you can know
  Flows, bandwidths, “Life-of-Packet” scenarios, specific common functions

## Slide 10: Simplified Categorization of Applications
Switching
Load Balancing
Firewall
Virtual Private Network
Quality of Service
Routing
Network Monitoring
Application Processing Complexity
Real Time
Virus Scanning
Ethernet
Header
IP Header
TCP Header
Payload Inspection
Packet Inspection Complexity

## Slide 11: Application
Forwarding (bridging/routing)
Protocol Conversion
In-system data movement (DMA+)
Encapsulation/Decapsulation to fabric/backplane devices
L4-L7 applications; content and/or flow-based
Security and Traffic Engineering
  Firewall, Encryption (IPSEC, SSL), Compression
  Rate shaping, QoS/CoS
Intrusion Detection /Prevention (IDS/IPS)
  Particularly challenging due to processing many state elements in parallel, unlike most other networking apps which are more likely single-path per packet/cell

## Slide 12: Acceleration Techniques (1)
Offload high-touch portions of applications from the uP
  Header parsing, checksums/CRCs, RegEx string search
Offload latency-intensive portions to reduce uP stall time
  Pointer-chasing in hash table lookups, tree traversals for e.g. routing LPM lookups, fetching of entire packet for high-touch work, fetch of candidate portion of packet for header parsing
Offload compute-intensive portions with specialized engines
  Crypto computation, RegEx string search computation, ATM CRC, packet classification (RegEx is mainly bandwidth and stall-intensive)
Provide efficient system management
  Buffer management, descriptor management, communications among units, timers, queues, freelists, etc.

## Slide 13: Acceleration Techniques (2)
Media processing (framing etc)
  Specialized units
Decouple hard real-time from budgeted-time
  meet per-packet/cell time budgets
  higher level processing via buffering (e.g. IP frag reass’y, TCP stream assembly and processing etc.)
Efficient communication among units
  Hardware and software must be well architected and designed to avoid this.
  Keep compute:communicate ratio high.

## Slide 14: Acceleration via Pipelining
Goal is to increase total processing time per packet/cell by providing a chain of pipelined processing units
  May be specialized hardware functions
  May be flexible programmable elements
  Might be lockstep or elastic pipeline
  Communication costs between units must be minimized to ensure a compute:communicate ratio that makes the extra stages a win
  Possible to hide some memory latency by having a predecessor request data for a successor in the pipeline
  If a successor can modify memory state seen by a predecessor then there is a “time-skew” consistency problem that must be addressed

## Slide 15: Acceleration via Parallelism
Goal is to increase total processing time per packet/cell by providing several processing units in parallel
  Generally these are identical programmable units
  May be symmetric (same program/microcode) or asymmetric
  If asymmetric, an early stage disaggregates different packet types to the appropriate type of unit (visualize a pipeline stage before a parallel farm)
  Keeping packets ordered within the same flow is a challenge
  Dealing with shared state among parallel units requires some form of locking and/or sequential consistency control which can eat some of the benefit of parallelism
Caveat; more parallel activity increases memory contention, thus latency

## Slide 16: Latency Hiding via Hardware Multi-Threading
Goal is to increase utilization of a hardware unit by sharing most of the unit, replicating some thread state, and switching to processing a different packet on a different thread while waiting for memory
  Specialized case of parallel processing, with less hardware
  Good utilization is under programmer control
  Generally non-preemptable (explicit yield model instead)
  As the ratio of memory latency to clock rate increases, more threads are needed to achieve the same utilization
  Has all of the consistency challenges of parallelism plus a few more (e.g. spinlock hazards)
  Opportunity for quick state sharing thread-to-thread, potentially enabling software pipelining within a group of threads on the same engine (threads may be asymmetric)

## Slide 17: Coprocessors: NP’s for NP’s
Sometimes specialized hardware is the best way to get the required speed for certain functions
  Many NP’s provide a fast path to external coproc’s; sometimes slave devices, sometime masters.
Variety of functions
  Encryption and Key Management
  Lookups, CAMs, Ternary CAMs
  Classification
  RegEx string searches (often on reassembled frames)
  Statistics gathering

## Slide 18: A Typical NP Architecture
General
Purpose
Processor
Memory
Interface
Network
DMA/Buffer
Physical
Interface
Coproc
DMA/BUS
Interface
Network
(i.e. GbE)
To main BUS (i.e. PCI-Express)
Memory
Coproc
Interface
Internal BUS

## Slide 19: Intel i960

## Slide 20: Intel i960
Embedded Processor
  I/O Processor
  Peer-to-peer
  Network Processor
PCI Interface
  One to the Main BUS
  Other to the Network Interface
Similar to Myrinet LANai
Further development leading into IXA?

## Slide 21: Intel IXA
Current Routers
  Involve general purpose CPUs
  Lots of ASICs (Application Specific Integrated Circuits ).
  The ASICs are necessary to keep up with the quantity and rate of the network traffic.
The StrongARM Core
  Replace the general purpose CPUs
Microengines
  Replace the bulk of the ASICs
Actually inherited IXA when they bought Digital.

## Slide 22: Intel IXP1200 NP
Very Low Power Parallel Processor Architecture with 7 232 MHz RISC processors
Hardware Based Multithreading on 6 RISC engines - Cost Effective
Distributed Data Storage Arch Supports Very Simple Programming Model
Active Memory Optimizations - High Performance With Commodity RAMs
Scalable Architecture
6 RISC Engines
StrongARM Core
PCI
SDRAM
SRAM
IX Bus
PCI
SDRAM
SRAM
IX Bus
Notes: This foil highlights the features of the IXP1200 which also exist in the IXP1240 and IXP1250 NPs
The wide range of packet handling and control functionality integrated into the IXP1200 Network Processor enables equipment developers to focus on development of new features and services

## Slide 23: Intel IXP 1200 Block Diagram

## Slide 24: IXP2400 Features
Customer ASICs
Utopia 1/2/3 or
POS-PL2/3
Interface
IXP2400
(Receive)
Host
CPU
(Optional)
ATM / POS PHY
or Ethernet MAC
Flash
Classification Accelerator
Micro-Engine
Cluster
Switch Fabric Port Interface
IXP2400
(Transmit)
DDR DRAM
2 GByte
QDR SRAM
20 Gbps
32 M Byte
Interface supports UTOPIA 1/2/3, SPI-3 (POS-PL3), and CSIX.
Four independent, configurable, 8-bit channels with the ability to aggregate channels for wider interfaces.
Media interface can support channelized media on RX and 32-bit connect to Switch Fabric over SPI-3 on TX (and vice versa) to support Switch Fabric option.
Two Quad Data Rate SRAM channels.
A QDR SRAM channel can interface to Co-Processors.
One DDR DRAM channel.
PCI 64/66 Host CPU interface.
Flash and PHY Mgmt interface.
Dedicated inter-IXP channel to communicate fabric flow control information from egress to ingress for dual chip solution.

## Slide 25: Microengine V2
CAM
128
GPR
Control
Store
4K
Instructions
128
GPR
Local
Memory
128 Next
Neighbor
128 S
Xfer Out
128 D
Xfer Out
Local
CSRs
CRC Unit
128 S
Xfer In
128 D
Xfer In
LM Addr 1
LM Addr 0
CRC remain
D-Push Bus
S-Push Bus
D-Pull Bus
S-Pull Bus
To Next Neighbor
From Next Neighbor
A_Operand
B_Operand
ALU_Out
P-Random #
Execution Data path
Multiply
Find first bit
Add, shift, logical
2 per CTX

## Slide 26: IXP 2400
Eight next generation Microengines (MEv2)
  Operating at 600MHz
  Automated packet scheduling and handling
  Local data store enables higher performance
Hardware acceleration for DiffServ, MPLS, and other QoS schemes
ATM Segmentation and Reassembly (SAR) support with headroom.
Intel® XscaleTM microarchitecture core operating at 600MHz

## Slide 27: Myrinet
Processor on Myrinet NIC
  Leading Interface card for Clustering
  Offload Network processing from main Processor
  One of the first “Network Processor”
Pipelined RISC processor
  General Purpose Processor
  Fully functional GCC with libraries
Interfaces
  Network (Myrinet – High BW/Low Latency)
  SRAM Memory Interface
  BUS Interface

## Slide 28: Myrinet Cards

## Slide 29: Flexibility
Physical Links are 10-Gigabit Ethernet
  10+10 Gigabits per second, full-duplex.
  Converted to other 10-Gigabit Ethernet PHYs.
  At the Data-Link level, the links may be either Ethernet or Myrinet
Software support
  MX-10G is the low-level message-passing system for the Myri-10G
  Includes ethernet emulation (TCP/IP, UDP/IP)
  10-Gigabit Ethernet drivers (A matter of Firmware)
Performance with the Myri-10G PCI-Express NICs
  Myrinet mode: 2µs MPI latency with 1.2 GBytes/s one-way
  10-Gigabit Ethernet mode, 9.6 Gbits/s TCP/IP rate

## Slide 30: Next
Next Lecture
  Hardware Accelerated Network Appliances
Laboratory
  Lab 5: Due on Oct 1 at 11:55pm
Reading Assignment
  DETER team, "Cyber defense technology networking and evaluation", In Communications of the ACM, Special issue on Emerging Technologies for Homeland Security, Vol. 47, Issue 3, pp 58-61, March 2004.