## Slide 1: CSCI 558L Lecture 2: Networking
Internetworking and Distributed Systems Laboratory
Young Cho
Department of Computer Science
University of Southern California
Slides adopted from Berkeley and Rice

## Slide 2: Networking
Communication
  Between Applications on different computers
Application Resource Needs/Demands
  Traffic data rate
  Traffic pattern (bursty or constant bit rate)
  Traffic target (multipoint or single destination, mobile or fixed)
  Delay sensitivity
  Loss sensitivity
Notes: Some example applications: video, audio, telnet, ftp, http, rpc – what are their needs

## Slide 3: Back in the Old Days…

## Slide 4: Packet Switching (Internet)
Packets

## Slide 5: Packet Switching
Interleave packets from different sources
Efficient: resources used on demand
  Statistical multiplexing
General
  Multiple types of applications
Accommodates bursty traffic
  Addition of queues

## Slide 6: Characteristics of Packet Switching
Store and forward
  Packets are self contained units
  Can use alternate paths – reordering
Contention
  Congestion
  Delay

## Slide 7: Internet[work]
Internet[work]
A collection of interconnected networks
Host: network endpoints (computer, PDA, light switch, …)
Router: node that connects networks
Internet vs. internet
Notes: What if want to communicate between hosts on different Ethernets? Internet as interoperability layer

## Slide 8: Internet
Heterogeneous Computer Networks
  Physical connection via routers and switches
Largest Conglomeration of Such Networks
LAN 1 and LAN 2 might be completely different,
totally incompatible LANs (e.g., Ethernet and WiFi,
802.11*, T1-links, DSL, …)

## Slide 9: Internet
Maps of the Internet

## Slide 10: Challenge
Many differences between networks
  Address formats
  Performance – bandwidth/latency
  Packet size
  Loss rate/pattern/handling
  Routing
How to translate between various network technologies?

## Slide 11: How To Find Nodes?
Internet
Computer 1
Computer 2
Need naming and routing

## Slide 12: Naming
What’s the IP address for www.usc.edu?
It is 128.125.253.136
Translates human readable names to logical endpoints
Local DNS Server
Computer 1

## Slide 13: Routing
R
R
R
R
R
H
H
H
H
R
R
H
R
Routers send packet towards destination
H: Hosts
R: Routers

## Slide 14: Meeting Application Demands
Reliability
  Corruption
  Lost packets
Flow and congestion control
Fragmentation
In-order delivery
Etc…

## Slide 15: Data Corruption
Internet
GET windex.html
GET index.html
Solution: Add a checksum
Problem: Data Corruption
0,9
9
6,7,8
21
4,5
7
1,2,3
6
X

## Slide 16: Bandwidth Bottleneck
Problem: Network Overload
Short bursts: buffer
What if buffer overflows?
  Packets dropped
  Sender adjusts rate until load = resources  “congestion control”
Solution: Buffering and Congestion Control

## Slide 17: Lost Packets
Internet
GET index.html
Problem: Lost Data
Internet
GET index.html
Solution: Timeout and Retransmit
GET index.html
GET index.html

## Slide 18: Large Data
Problem: Packet size
Solution: Fragment data across packets
On Ethernet, max IP packet is 1.5kbytes
Typical web page is 10kbytes
GET
inde
x.ht
ml
GET index.html

## Slide 19: Out of Order Packets
Solution: Add Sequence Numbers
Problem: Out of Order
GET
x.ht
inde
ml
GET x.htindeml
GET index.html
ml
4
inde
2
x.ht
3
GET
1

## Slide 20: An Internet Connection

## Slide 21: Lots of Functions Needed
Link
Multiplexing
Routing
Addressing/naming (locating peers)
Reliability
Flow control
Fragmentation
Etc….

## Slide 22: What is Layering?
Modular approach to network functionality
Example:
Link hardware
Host-to-host connectivity
Application-to-application channels
Application

## Slide 23: Protocols
Module in layered structure
Set of rules governing communication
  Applications
  Hosts
  Routers
Protocols define:
  Interface to higher layers (API)
  Interface to peer
    Format and order of messages
    Actions taken on receipt of a message
Notes: Human analogy – social customs

## Slide 24: Layering Characteristics
Services
  Each layer relies on services from layer below
  Each layer exports services to layer above
  Provides interface that defines interaction
Modularity
  Hides implementation
  Layers can change without disturbing other layers (black box)

## Slide 25: Layering
Host
Host
Application
Transport
Network
Link
User A
User B
Layering: technique to simplify complex systems

## Slide 26: OSI Model: 7 Protocol Layers
Physical: how to transmit bits
Data link: how to transmit frames
Network: how to route packets
Transport: how to send packets end2end
Session: how to tie flows together
Presentation: byte ordering, security
Application: everything else

## Slide 27: OSI Layers and Locations
Switch
Router
Host
Host
Application
Transport
Network
Data Link
Presentation
Session
Physical

## Slide 28: Layer Encapsulation
Get index.html
Connection ID
Source/Destination
Link Address
User A
User B

## Slide 29: Remnants of Layering
Redundancy
  Layer N may duplicate lower level functionality (e.g., error recovery)
  Layers may need same info (timestamp, MTU)
Consequences
  For assurance and guarantee
  May hurt performance

## Slide 30: Conclusion
Beginnings of Internet
  Purpose is to provide robust, scalable, and effective network
  Theoretical foundations for packet networks in 1962: Kleinrock
  Hierarchical routing in 1970’s : Kleinrock
  ARPANET connecting UCLA and SRI on Oct 29, 1969
  The rest is a complex web of history (w/ many proclaimed fathers)
  Conclusion: it works pretty well!
Internet Governance
  USC – Information Sciences Institute
  Internet Corporation for Assigned Names and Numbers
  ICANN assigns unique identifiers for use on the Internet
    including domain names, Internet Protocol (IP) addresses, application port numbers in the transport protocols, and many other parameters

## Slide 31: Next
Next Lecture: Ethernet and IP
Projects
  Team sign-up sheet
  Working on the Emulab Tutorials
Reading Assignment:
  The DARPA Internet Protocol Suite
  Slides and Q&A
Students Added and Dropped