## Slide 1: CSCI 558L Lecture 3: Computer Networking and Ethernet
Internetworking and Distributed Systems Laboratory
Young Cho
Department of Computer Science
University of Southern California
Slides adopted from Berkeley and Rice

## Slide 2: Lost Packets
Internet
GET index.html
Problem: Lost Data
Internet
GET index.html
Solution: Timeout and Retransmit
GET index.html
GET index.html

## Slide 3: Large Data
Problem: Packet size
Solution: Fragment data across packets
On Ethernet, max IP packet is 1.5kbytes
Typical web page is 10kbytes
GET
inde
x.ht
ml
GET index.html

## Slide 4: Out of Order Packets
Solution: Add Sequence Numbers
Problem: Out of Order
GET
x.ht
inde
ml
GET x.htindeml
GET index.html
ml
4
inde
2
x.ht
3
GET
1

## Slide 5: Lots of Functions Needed
Link
Multiplexing
Routing
Addressing/naming (locating peers)
Reliability
Flow control
Fragmentation
Etc….

## Slide 6: What is Layering?
Modular approach to network functionality
Example:
Link hardware
Host-to-host connectivity
Application-to-application channels
Application

## Slide 7: Protocols
Module in layered structure
Set of rules governing communication
  Applications
  Hosts
  Routers
Protocols define:
  Interface to higher layers (API)
  Interface to peer
    Format and order of messages
    Actions taken on receipt of a message
Notes: Human analogy – social customs

## Slide 8: Layering Characteristics
Services
  Each layer relies on services from layer below
  Each layer exports services to layer above
  Provides interface that defines interaction
Modularity
  Hides implementation
  Layers can change without disturbing other layers (black box)

## Slide 9: Layering
Host
Host
Application
Transport
Network
Link
User A
User B
Layering: technique to simplify complex systems

## Slide 10: Open System Interconnection Reference Model
From computer desktop encyclopedia © 2004

## Slide 11: Lower Layers Networking
Physical Layer
  Types of physical links
  Configurations and scalability
Arbitration/Control of Medium
  Transmitting with address
  Fairness and Performance on Transmission
Network Layer
  Routing over heterogeneous networks

## Slide 12: Physical Layer
Types of Links
  Wires/Wireless
  Optics, Copper, Acoustics, RF and etc.
Configurations
  Bus, Ring, Star, and etc.
  Bandwith/Latency/Cost
Scalability
  Composition
  Maximum number of nodes

## Slide 13: Medium Access Control
Fixed assignment
  Each node gets a slice of the bandwidth
  Examples: TDMA, FDMA, CDMA
    popular in wireless devices
Reservation-based
  Reserve the channel when using
  Example: Token Ring
Contention-based
  Nodes contend and recover from collisions
  Examples: Aloha, Ethernet

## Slide 14: OSI Layers and Locations
Switch
Router
Host
Host
Application
Transport
Network
Data Link
Presentation
Session
Physical

## Slide 15: Layer Encapsulation
Get index.html
Connection ID
Source/Destination
Link Address
User A
User B

## Slide 16: Remnants of Layering
Redundancy
  Layer N may duplicate lower level functionality (e.g., error recovery)
  Layers may need same info (timestamp, MTU)
Consequences
  For assurance and guarantee
  May hurt performance

## Slide 17: Time Division Multiple Access
from wikipedia

## Slide 18: Token Ring
IBM in early 80’s as a new LAN architecture
  Nodes connected into a ring
  Special message called a token is passed around
    When nodes gets the token it can transmit for a time
    Every node gets an equal opportunity to send
  IEEE 802.5 standard for Token Ring
Predictability, fairness and reliability
  Designed to run at either 4Mbps and 16Mbps
Still used but beaten out by Ethernet

## Slide 19: Aloha Packet Radio Network
Early RF broadcast network developed at University of Hawaii1970
Designed to interconnect 7 campuses of the U of H
Central Computing Center served as hub
  Senders send the data when necessary
  Receiver sends an ACK for data, Timeout for ACK signals that there was a collision
  When collision, sender will resend data after a random back-off time
Utilization (fraction of transmitted frames avoiding collision for N nodes)
  Max utilization = 18%
Slotted Aloha (dividing transmit time into windows)
  Max utilization increased to 36%
Computing
Center
Campus A
Campus B
413 MHz
413 MHz
407 MHz
407 MHz
Throughput 9600 bps
Frame Size 704 bits

## Slide 20: Focus: Ethernet
History
  Developed by Bob Metcalfe at Xerox PARC in mid-1970s
  Roots in Aloha packet-radio network
  Standardized by Xerox, DEC, and Intel in 1978
  LAN standards define MAC and physical layer connectivity
    IEEE 802.3 (CSMA/CD - Ethernet) standard – originally 2Mbps
    IEEE 802.3u standard for 100Mbps Ethernet
    IEEE 802.3z standard for 1,000Mbps Ethernet
    IEEE 802.3ax-xxxx standard for 10Gbps Ethernet
CSMA/CD: Ethernet’s Media Access Control (MAC) policy
  CS = carrier sense
    Send only if medium is idle
  MA = multiple access
  CD = collision detection
    Stop sending immediately if collision is detected

## Slide 21: Ethernet Standard
802.3 standard defines both MAC and physical layer
Metcalfe’s original Ethernet Sketch

## Slide 22: Ethernet Technologies: 10Base2
10: 10Mbps; 2: under 185 (~200) meters cable length
Thin coaxial cable in a bus topology
Repeaters used to connect multiple segments
  Repeater repeats bits it hears on one interface to its other interfaces: physical layer device only!

## Slide 23: 10BaseT and 100BaseT
10/100 Mbps rate
T stands for Twisted Pair
Hub(s) connected by twisted pair facilitate “star topology”
  Distance of any node to hub must be < 100M

## Slide 24: Physical Layer Configurations for 802.3
Data rate (10Mbps-10Gbps)
Signaling method (base, broad)
  Baseband: Digital signaling
  Broadband: Analog signaling
Cabling (2, 5, T, F, S, L)
  5 - Thick coax (original Ethernet cabling)
  F – Optical fiber
  S – Short wave laser over multimode fiber
  L – Long wave laser over single mode fiber

## Slide 25: Ethernet Overview
Most popular packet-switched LAN technology
Bandwidths: 10Mbps-10Gbps
  40-100 Gbps in the works (draft stage)
    Products being developed and announced (Juniper)
    Testing equipments (Ixia, Spirent, Agilent, and etc.)
Bus length
  Traditionally 500m segments with 4 repeaters
  Depends on PHY
Bus and Star topologies are used to connect hosts
  Hosts attached via Ethernet transceiver or hub or switch
    Detects line state and sends/receives signals
  Hubs are used to facilitate shared connections
    All hosts on an Ethernet are competing for access
  Switches
    Breaks the original model
    Used by most higher speed Ethernet (1+ Gbps)
Ethernet by definition is a broadcast protocol
  Any signal can be received by all hosts
  Switching enables individual hosts to communicate

## Slide 26: Switched Ethernet
Switches forward frames based on MAC addresses
  Not a bus
  Simple forwarding tables are maintained
Highly Scalable
  Options for many interfaces
  Full duplex operation (send/receive frames simultaneously)
Connect 2+ “segments” by copying data frames
  Switches only copy data when needed (less overhead over repeaters)
Higher link bandwidth
  No Collisions at each links
  Port can have contention (buffers are used)
Much greater aggregate bandwidth
  Separate segments can send at once

## Slide 27: Ethernet Frames
Network layer packets are transmitted by encapsulating
Preamble is a sequence of 7 bytes, each set to “10101010”
  Used to synchronize receiver before actual data is sent
Medium Access Control Addresses
  unique, 48-bit unicast address assigned to each adapter
    example: 8:0:e4:b1:2
    Each manufacturer gets their own address range
  broadcast: all 1s
  multicast: first bit is 1
Type field
  Key to indicate higher level protocol
Body can contain up to 1500 bytes of data
  Jumbo packets go up to 9000 bytes
Dest
addr
64
48
32
CRC
Preamble
Src
addr
Type
Body
16
48

## Slide 28: Ethernet’s MAC Algorithm
Different from Aloha
  Aloha sent packets regardless of others
  Long distances and different communication coverage
Ethernet uses Carrier Sense Multiple Access CSMA/CD
  Listens to line before/during sending
  CD – Collision Detection
  Not CA – Collision Avoidance (Radio Spectrum)
If line is idle (no carrier sensed)
  send packet immediately
  upper bound message size of 1500 bytes
  must wait 9.6us between back-to-back frames
If line is busy (carrier sensed)
  wait until idle and transmit packet immediately
If collision detected
  Stop sending and jam signal
  Try again later

## Slide 29: State Diagram for CSMA/CD
Sense Carrier
Discard Packet
Send
Detect Collision
Jam channel b=CalcBackoff(); wait(b);
attempts++;
No
attempts < 16
attempts == 16
Packet?

## Slide 30: Collisions
Collisions are caused when two adaptors transmit at the same
time (adaptors sense collision based on voltage differences)
  Both found line to be idle
  Both had been waiting to for a busy line to become idle
A
B
A
B
A starts at
time 0
Message almost
there at time T when
B starts – collision!
How can we be sure A knows about the collision?

## Slide 31: Collision Detection
How can A know that a collision has taken place?
  There must be a mechanism to insure retransmission on collision
  A’s message reaches B at time T
  B’s message reaches A at time 2T
  So, A must still be transmitting at 2T
IEEE 802.3 specifies max value of 2T to be 51.2us
  This relates to maximum distance of 2500m between hosts
  At 10Mbps it takes 0.1us to transmit one bit so 512 bits (64B) take 51.2us to send
  So, Ethernet frames must be at least 64B long
    14B header, 46B data, 4B CRC
    Padding is used if data is less than 46B
Send jamming signal after collision is detected to insure all hosts see collision
  48 bit signal

## Slide 32: Exponential Backoff
If a collision is detected, delay and try again
Delay time is selected using binary exponential backoff
  1st time: choose K from {0,1} then delay = K * 51.2us
  2nd time: choose K from {0,1,2,3} then delay = K * 51.2us
  nth time: delay = K x 51.2us, for K=0..2n – 1
    Note max value for k = 1023
  give up after several tries (usually 16)
    Report transmit error to host
If delay were not random, then there is a chance that sources would retransmit in lock step
Why not just choose from small set for K
  This works fine for a small number of hosts
  Large number of nodes would result in more collisions

## Slide 33: Experiences with Ethernet
Ethernets work best under light loads
  Utilization over 30% is considered heavy
    Network capacity is wasted by collisions
Most networks are limited to about 200 hosts
  Specification allows for up to 1024
Most networks are much shorter
  5 to 10 microsecond RTT
Transport level flow control helps reduce load (number of back to back packets)
Ethernet is inexpensive, fast and easy to administer!

## Slide 34: Fast and 1+ Gigabit Ethernet
Fast Ethernet (100Mbps) has technology very similar to 10Mbps Ethernet
  Uses different physical layer encoding (4B5B)
  Many NIC’s are 10/100 capable
    Can be used at either speed
1 Gigabit Ethernet
  Compatible with lower speeds
  Uses standard framing and CSMA/CD algorithm
  Distances are severely limited
  Commoditized (integrated on to the motherboards)
  What are the bandwidth limitation? True 1Gbps?
10+ Gigabit Ethernet
  Mostly incompatible with lower speeds
  Special PHY needed
  Cost is going down for 10Gbps (~$500-$1000/NIC)
  Expensive appliances

## Slide 35: Ethernet Problems
Ethernet’s peak utilization is pretty low
Peak throughput worst with
  More hosts
    More collisions needed to identify single sender
  Smaller packet sizes
    More frequent arbitration
  Longer links
    Collisions take longer to observe, more wasted bandwidth
  Efficiency is improved by avoiding these conditions

## Slide 36: Ethernet: The Network of Choice
Low Price
Lots of Support
Performance
High Availability
Ease of use
High Scalability
Historical

## Slide 37: Minimalist Approach for Higher Level
Dumb network
  IP provide minimal functionalities to support connectivity
    Addressing, forwarding, routing
Smart end system
  Transport layer or application performs more sophisticated functionalities
    Flow control, error control, congestion control
Advantages
  Accommodate heterogeneous technologies (Ethernet, modem, satellite, wireless)
  Support diverse applications (telnet, ftp, Web, X windows)
  Decentralized network administration

## Slide 38: Next
Next Lecture: Internet Protocol
  Post Your Group Information
    Project Group Forum
  Laboratory 2
    Socket Programming Tutorial
    Due September 6, 2012 at 11:55pm
  Reading Assignment
    Narten, T., "Internet Routing", ACM SigCom 89.
    4 powerpoint/pdf slides
    1 title slide, 2 summary slides, 1 Q&A slide
    Summarizing the content of the paper (include at least 1 hand drawn picture by you to describe each slide).
    Also make one slide containing one exam question and answer based on the main concept of the paper. Please turn the slides in by September 8, 2012 11:55pm for a full credit.