## Slide 1: CSCI 558L Lecture 4: Internet Protocol
Internetworking and Distributed Systems Laboratory
Young Cho
Department of Computer Science
University of Southern California
Slides adopted from Berkeley and Rice

## Slide 2: Open System Interconnection Reference Model
From computer desktop encyclopedia © 2004

## Slide 3: Internet Protocol
Interconnect many networks
Hide underlying technology
  IP is the “compatibility layer”
Hourglass architecture
  All hosts and routers run IP
  Stateless architecture
Trade-off
  No assumptions
  No guarantees
Technology
Applications
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP
ethernet PPP…
CSMA async sonet...
copper fiber radio...

## Slide 4: IPv4 Packet Structure
Ver
IHL
Type of service
Total length
Identification
Flags
Fragment offset
Time to live
Header checksum
Protocol
Source address
Destination address
Option + Padding
Ver
IHL
Differentiated Services
Total length
Identification (frag id)
Flags (frag)
Fragment offset
Time to live
Header checksum
(next) Protocol
Source address
Destination address
Option + Padding
Source Port
Destination Port
Sequence Number
Offset
Acknowledgement Number
U A P R S F
Window
Checksum
Option + Padding
Reserved
Urgent pointer
Source Port
Destination Port
Sequence Number
Offset
Acknowledgement Number
U A P R S F
Window
Checksum
Option + Padding
Data
Reserved
Urgent pointer

## Slide 5: Fields of the IPv4 Header
Version (4 bits)
  4 for IPv4, 6 for IPv6
Header length (4 bits)
  length of IP header, in multiples of 4 bytes
DS/ECN field (1 byte)
  This field was previously called as Type-of-Service (TOS) field. The role of this field has been re-defined, but is “backwards compatible” to TOS interpretation
  Differentiated Service (DS) (6 bits):
    Used to specify scalable service levels (unclear)
  Explicit Congestion Notification (ECN) (2 bits):
    New feedback mechanism used by TCP

## Slide 6: Fields of the IP Header
Identification (16 bits)
  Unique identification of a datagram from a host.
  Incremented whenever a datagram is transmitted
Flags (3 bits)
  First bit always set to 0
  DF bit (Do not fragment)
  MF bit (More fragments)
Fragment Offset (13 bits)
  This field indicates where in the datagram this fragment belongs

## Slide 7: Fields of the IP Header
Time To Live (TTL) (1 byte):
  Specifies longest paths before datagram is dropped
  Role of TTL field: Ensure that packet is eventually dropped when a routing loop occurs
  Used as follows:
  Sender sets the value (e.g., 64)
  Each router decrements the value by 1
  When the value reaches 0, the datagram is dropped

## Slide 8: Fields of the IP Header
Protocol (1 byte):
  Specifies the higher-layer protocol.
  Used for demultiplexing to higher layers.
Header checksum (2 bytes):
  16-bit long checksum for the header of the datagram

## Slide 9: Fields of the IP Header
Options:
  Security restrictions
  Record Route: each router that processes the packet adds its IP address to the header.
  Timestamp: each router that processes the packet adds its IP address and time to the header.
  (loose) Source Routing: specifies a list of routers that must be traversed.
  (strict) Source Routing: specifies a list of the only routers that can be traversed.
Padding:
  Padding bytes are added to ensure that header ends on a 4-byte boundary

## Slide 10: Fragmentation
IP packets can be 64KB
  Different link-layers have different MTUs
  Split IP packet into multiple fragments
    IP header on each fragment
    Various fields in header to help process
    Intermediate router may fragment as needed
Where to do reassembly?
  End nodes – avoids unnecessary work
  Dangerous to do at intermediate nodes
    Buffer space
    Multiple paths through network

## Slide 11: Fragmentation Disadvantages
Uses resources poorly
  Forwarding costs per packet
  Best if we can send large chunks of data
  Worst case: packet just bigger than MTU
Poor end-to-end performance
  Loss of a fragment
Reassembly is hard
  Buffering constraints

## Slide 12: IP Address Problem (1991)
Address space depletion
  In danger of running out of classes A and B
Why?
  Class C too small for most domains
  Very few class A – IANA (Internet Assigned Numbers Authority) very careful about giving
  Class B – greatest problem
    Sparsely populated – but people refuse to give it back

## Slide 13: IP Address Utilization (’98)
http://www.caida.org/outreach/resources/learn/ipv4space/

## Slide 14: IPv4 Routing Problems
Core router forwarding tables were growing large
  Class A: 128 networks, 16M hosts
  Class B: 16K networks, 64K hosts
  Class C: 2M networks, 256 hosts
32 bits does not give enough space encode network location information inside address – i.e., create a structured hierarchy

## Slide 15: Mitigation Efforts
Classless Inter-Domain Routing (CIDR)
Network address translation (NAT)
Use of private network addressing
Name-based virtual hosting of web sites
Tighter control by regional Internet registries on the allocation of addresses to local Internet registries
Network renumbering and subnetting to reclaim large blocks of address space allocated in the early days of the Internet, when the Internet used inefficient classful network addressing

## Slide 16: CIDR
Assign multiple class C addresses
Assign consecutive blocks
RFC1338 – Classless Inter-Domain Routing (CIDR)

## Slide 17: Classless Inter-Domain Routing
Do not use classes to determine network ID
Assign any range of addresses to network
  Use common part of address as network number
  e.g., addresses 192.4.16 - 196.4.31 have the first 20 bits in common. Thus, we use this as the network number
  netmask is /20, /xx is valid for almost any xx
Enables more efficient usage of address space (and router tables)

## Slide 18: NAT
Network Address Translation (NAT)
Alternate solution to address space
  Kludge (but useful)
Sits between your network and the Internet
Translates local network layer addresses to global IP addresses
Has a pool of global IP addresses (less than number of hosts on your network)

## Slide 19: NAT Illustration
Global Internet
Private
Network
Pool of global IP addresses
Operation: Source (S) wants to talk to Destination (D):
  Create Sg-Sp mapping
  Replace Sp with Sg for outgoing packets
  Replace Sg with Sp for incoming packets
D & S can be just IP addresses or IP addresses + port #’s
P
G
Dg
Sp
Data
NAT
Destination
Source
Dg
Sg
Data

## Slide 20: IPv6
Scale – addresses are 128bit
  Approximately 340 undecillion or 3.4×1038
  Header size?
Simplification
  Removes infrequently used parts of header
  40byte fixed size vs. 20+ byte variable
IPv6 removes checksum
  Relies on upper layer protocols to provide integrity
IPv6 eliminates fragmentation
  Requires path MTU discovery
  Requires 1280 byte MTU

## Slide 21: Features of IPv6
Larger Address Space
Aggregation-based address hierarchy
– Efficient backbone routing
Efficient and Extensible IP datagram
Stateless Address Autoconfiguration
Security (IPsec mandatory)
Mobility

## Slide 22
40
bytes
20
bytes
IPv4
IPv6
0
15
16
31
vers hlen TOS total length
identification flags flag-offset
TTL protocol header checksum
source address
destination address
options and padding
vers traffic class flow-label
payload length next header hop limit
source address
destination address
Removed (6)
ID, flags, flag offset
TOS, hlen
header checksum
Changed (3)
Added (2)
Expanded
total length => payload
protocol => next header
TTL => hop limit
traffic class
flow label
address 32 to 128 bits
Header comparison

## Slide 23: Changes
Streamlined
  Fragmentation fields moved out of base header
  IP options moved out of base header
  Header Checksum eliminated
  Header Length field eliminated
  Length field excludes IPv6 header
  Alignment changed from 32 to 64 bits
Revised
  Time to Live to Hop Limit
  Protocol to Next Header
  Precedence & TOS to Traffic Class
  Addresses increased 32 bits to 128 bits
Extended
  Flow Label field added

## Slide 24: Extension Headers
Routing – Extended routing, like IPv4 loose list of routers to visit
Fragmentation – Fragmentation and reassembly
Authentication – Integrity and authentication, security
Encapsulation – Confidentiality
Hop-by-Hop Option – Special options that require hop-by-hop processing
Destination Options – Optional information to be examined by the destination node

## Slide 25: Extension Headers
next header =
TCP
TCP header + data
IPv6 header
next header =
Routing
TCP header + data
Routing header
next header =
TCP
IPv6 header
next header =
Routing
fragment of TCP
header + data
Routing header
next header =
Fragment
Fragment header
next header =
TCP
IPv6 header

## Slide 26: Extension Headers
Generally processed only by node identified in IPv6 Destination Address field
  much lower overhead than IPv4 options processing
  exception: Hop-by-Hop Options header
Eliminated IPv4’s 40-byte limit on options
  in IPv6, limit is total packet size, or Path MTU in some cases
Currently defined extension headers:
  Fragment, Hop-by-Hop Options, Routing, Authentication, Encryption, Destination Options

## Slide 27: Fragment Header
IPv6 fragmentation & reassembly is an end-to-end
  Routers do not fragment packets
  If packet is too big they send ICMP "packet too big"
Next Header
Original Packet Identifier
Reserved
Fragment Offset
0 0 M

## Slide 28: 128-bit IPv6 Address
3FFE:085B:1F1F:0000:0000:0000:00A9:1234
8 groups of 16-bit hexadecimal numbers separated by “:”
3FFE:85B:1F1F::A9:1234
:: = all zeros in one or more group of 16-bit hexadecimal numbers
Leading zeros can be removed

## Slide 29: Text Representation
"Preferred" form: 1080:0:FF:0:8:800:200C:417A
Compressed form: FF01:0:0:0:0:0:0:43
becomes FF01::43
IPv4-mapped: 0:0:0:0:0:FFFF:10.1.68.3
or ::FFFF:10.1.68.3

## Slide 30: Address Allocation
The allocation process was recently updated by the registries:
  International Assigned Numbers Authority (IANA) allocates from 2001::/16 to regional registries
  Each regional registry allocation is a ::/23
  ISP allocations from the regional registry is a ::/36 (immediate allocation) or ::/32 (initial allocation) or shorter with justification
  Policy expectation that an ISP allocates a ::/48 prefix to each customer
2001
0410
ISP prefix
Site prefix
Subnet prefix
/32
/48
/64
Registry
/23
Interface ID
Notes: The generic allocation process is:
  IANA allocates 2001::/16 to registries from the full address space
  Slow-start allocation process:
    Each registry gets a /23 prefix from IANA, within the 2001::/16 space
    Registry allocates an initial /35 prefix to a new IPv6 ISP
    ISP allocates a /48 prefix (out of the /35) to each customer
The slow-start allocation process is there to minimize the initial space given to an ISP. This enforces the conservation of addresses.
Cisco managed to receive a /35 prefix: 2001:0420::/35.

## Slide 31: Preview: Transport vs. Network
Network layer: logical communication between hosts
Transport layer: logical communication between processes
  relies on, enhances, network layer services
Postal service analogy:
kids sending letters to other kids
processes = kids
app messages = letters in envelopes
hosts = houses
transport protocol = two specific kids
network-layer protocol = postal service

## Slide 32: Internet transport-layer protocols
Reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
Unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
Services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 33: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header
no congestion control: UDP can blast away as fast as desired

## Slide 34: TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 35: TCP seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
simple telnet scenario

## Slide 36: Laboratory 4: Fast and Reliable FTP
Part A
  Each group split into 2 subgroups
    Competing within each group
    Demo both methods on Sept 17th
    Full credit for >20 Mbps on 100Mbps/200ms/20% loss
  Automated script to determine winner
    Extra credit, if your script is used in Part B
100 Mbps
200ms RTT
20% packet loss

## Slide 37: Laboratory 4: Fast and Reliable FTP
Part B
  Each group merge the best techniques
  Tournament Qualification: >40 Mbps (full credit)
The Tournament
  September 24th: tournament at demo
  September 25th: the finalists compete in class
  The winner(s) will get extra credit
CSCI 558L FTP Tournament

## Slide 38: Next
Next Lecture: Network Performance
  Laboratory 2 & 3
    Socket Programming Tutorial
    Due September 6, 2012 at 11:55pm
    Measuring Network Performance
    Due September 8, 2012 at 11:55pm
Laboratory 4: Fast and Reliable FTP
  Part A – Due Sept 15th, demo 17th
  Part B – Demo Sept 24th ,Finalists Compete 25th
  Reading Assignment
    Narten, T., "Internet Routing", ACM SigCom 89.
    Please turn the slides in by September 8, 2011 11:55pm for a full credit.