## Slide 1: CSCI 558L Lecture 5: Network Performance
Internetworking and Distributed Systems Laboratory
Young Cho
Department of Computer Science
University of Southern California

## Slide 2: Bandwidth Metrics
Network Measurement Working Group
  Bandwidth Capacity
  Achievable Bandwidth (Throughput)
  Bandwidth Utilization
  Available Bandwidth
Bulk Transfer Capacity (RFC 3148)
  BTC = data_sent / elapsed_time
  i.e. the throughput of a persistent TCP transfer
Range of Metric Usage
  End-to-end
  Hop-to-hop

## Slide 3: Bandwidth Metrics
Bandwidth Capacity
  The maximum amount of data per time unit that the link or path has available, when there is no competing traffic
  The link with the minimum transmission rate determines the capacity
Achievable bandwidth (Throughput)
  The maximum amount of data per time unit that a link or path can provide to an application, given the current utilization, the protocol and operating system used, and the end-host performance capability and load
  Hardware/software configuration on the end hosts actually limit the achievable bandwidth delivered to the application.
Bandwidth Utilization
  The aggregate capacity currently being consumed
Available Bandwidth
  Available Bandwidth = Bandwidth Capacity – Bandwidth Utilization

## Slide 4: Bulk Transfer Capacity
Maximum Bulk Transfer
  Sending as much packets as possible, limiting other traffic
Simulating “steady state”
  Persistent flow, taking considerable time and overhead
Assumption
  Ideal TCP implementation
  Actually, this doesn’t exist
  Ultimately, a variant of achievable bandwidth.

## Slide 5: Passive vs. Active measurement
Active Measurement
  Tools actively send probing packets into the network
  Overhead introduced
Passive Measurement
  Tools monitors the passing traffic without interfering
  Less reliable than active – cannot selectively measure all aspect of bandwidth

## Slide 6: Measurement Techniques
Receiver-based (end-to-end)
  Usually use the one-direction TCP stream to probe the path bandwidth
  Advantage
    More accurate than sender-based technique
  Disadvantage
    Difficult to deploy
    The clock have to be synchronized at two ends
Sender-based (echo-based)
  Force the receiver to reply the ICMP query, UDP echo or TCP-FIN
  Advantage
    Flexible deployment
    Clock needn’t synchronized at two ends.
  Disadvantage:
    ICMP and UDP echo packets are rate-limited or filtered out by some routers
    Round-trip is influenced by cross-traffic than that of one-way delay
    Response packets may come back through a different path

## Slide 7: Measurement Technique Examples
Packet Dispersion technology
  Packet pair and packet train
  Self-Loading Periodic streams (SLOPS)
Variable Packet Size (VPS) technology
  VPS even/odd
  Tailgating technique

## Slide 8: Packet Dispersion Technique
Sender sends two same-size packets back-to-back from source to sink.
The packets will reach the sink dispersed by the transmission delay of the bottleneck links if there is no cross traffic
Measuring the dispersion can infer the bottleneck link bandwidth capacity.
Note: Bottleneck link can refer to the link with smallest transmission rate, it’s also can refer to the link with minimum available bandwidth. We refer the bottleneck link to the first case.

## Slide 9: Packet Dispersion Technique
FOR MORE INFO...
Bprobe and cprobe http://cs-people.bu.edu/carter/tools/Tools.html
Nettest http://www-didc.lbl.gov/pipechar
Pathrate http://www.cc.gatech.edu/fac/Constantinos.Dovrolis
Pipechar http://www-didc.lbl.gov/pipechar
SProbe http://sprobe.cs.washington.edu
Tool Name | Method | Protocol | Metrics
bprobe | Packet pair | ICMP | Bandwidth Capacity
cprobe | Packet pair | ICMP | Bandwidth utilization
Netest | Packet pair | UDP | Bandwidth capacity
Pathrate | Packet pair, packet train | UDP | Bandwidth capacity
Pipechar | Packet train | UDP | Available bandwidth
Sprobe | Packet pair | TCP | Bandwidth capacity

## Slide 10: Self-Loading Periodic Streams(SLOPS)
Sender sends series of packets to the sink at the rate of larger than the bottleneck link available bandwidth
Every packets get a timestamp at sender side.
Compare the difference of successive packets timestamp and their arrival times to infer the available bandwidth.
Rate-adjustment adaptive algorithm to converge to the available bandwidth.
FOR MORE INFO...
Pathload http://www.cc.gatech.edu/fac/Constantinos.Dovrolis

## Slide 11: Variable Packet Size (VPS) Technique
Step1
  Sender set TTL=1
  send out the packet
  wait for the ICMP TTL-exceeded packet
Step2
  Upon receiving ICMP
  Estimate the RTT multiple times for various size packets
  The minimum RTT of various packets are believed to be the valid sample.
Step3
  The first link capacity is C=1/b , b is slope of RTT graph.
Set the TTL=2,3…n, repeat the process of step1 to 3, to Calculate the C=1/ bi – bi-1

## Slide 12: VPS technique cont.

## Slide 13: VPS Technology
Bing http://www.cnam.fn/reseau/bing.html
Clink http://rocky.wellesley.edu/downey/clink/
Pchar http://www.emplyees.org/~bmah/software/pchar
Nettimer http://mosquitonet.stanford.edu/~laik/project/nettimer
Pathchar ftp://ftp.ee.lbl.gov/pathchar/
Tool Name | Protocol | Metrics | Path/Per-link
bing | ICMP | Bandwidth capacity, loss, delay | Path
clink | UDP | Bandwidth capacity, Loss | Path
Pchar | UDP, ICMP | Bandwidth capacity, Loss, delay | Per-link
Nettimer | TCP | Bandwidth capacity | Per-link
pathchar | UDP, ICMP | Bandwidth capacity, Loss, delay | Per-link
FOR MORE INFO...

## Slide 14: TCP Simulation and Path Flooding
TCP simulation
  Simulates the TCP of using slow-start algorithm
Path flooding
  Injects TCP/UDP packets into the net as fast as possible within the specific time.
Associated with Bulk Transfer Capacity

## Slide 15: TCP Simulation and Path Flooding
Tool Name | Method | Protocol | Metrics | Path/Per-link
TReno | TCP simulation | UDP, ICMP | BTC | Path
ttcp | Path flooding | TCP, UDP | Achievable bandwidth | Path
iperf | Path flooding | TCP, UDP | Bandwidth capacity, Loss | Path
Netperf | Path flooding | TCP, UDP | BTC, delay throughput | Path
TReno http://www.psc.edu/networking/treno_info.html
Iperf http://dast.nlanr.net/Project/Iperf
Netperf http://www.netperf.org/netperf/NetperfPage.html
ttcp ftp://ftp.arl.mil/pub/ttcp/
FOR MORE INFO...

## Slide 16: Laboratory 4
Purpose
  Learn to use iperf to measure performance
  Learn to configure and use DETER
  Learn the effects of Bandwidth and Delay
  Learn to adjust network specific OS kernel configurations to increase performance
Submission
  Create a document with tables, graphs, and paragraphs describing the answers to all the questions
  Submit via moodle

## Slide 17: IPERF
Website
  http://dast.nlanr.net/Projects/Iperf/
Format
  server side
    iperf -s -%
    Iperf -s -V
  client side
    iperf -c <server address> -%
    iperf -c <server IPv6 address>

## Slide 18: Command line option
-s : Run in server mode
-D : Run the server as a daemon
-w
  TCP : window size (Default ：8K for Windows 32.5K for FreeBSD)
  UDP: buffer size (Default ：8K for Windows 9K for FreeBSD)
-f
  Specifying the format to print bandwidth numbers in
'b' = bits/sec 'B' = Bytes/sec
'k' = Kbits/sec 'K' = KBytes/sec
'm' = Mbits/sec 'M' = MBytes/sec
'g' = Gbits/sec 'G' = GBytes/sec
(Default) 'a' = adaptive bits/sec 'A' = adaptive Bytes/sec

## Slide 19: Command line option

## Slide 20: Command line option
-l: The length of buffers to read or write.
  ( Default 8KB for TCP, 1470 bytes for UDP)
  Buffer Delay is unfavorable to Real-Time Application.
-i: Sets the interval time.
-u: Use UDP rather than TCP.
-C: Compatibility mode allows for use with older version of iperf
-N: nodelay

## Slide 21: Command line option

## Slide 22: Command line option

## Slide 23: Command line option
Client specific options
-b：for UDP, bandwidth to send at in bits/sec.
(default 1 Mbit/sec, implies -u)
-n：number of bytes to transmit (instead of -t)
-t：time in seconds to transmit for (default 10 secs)

## Slide 24: Command line option

## Slide 25: Command line option
-P：number of parallel client threads to run .

## Slide 26: Command line option
-B: Bind to host
  useful on multi-homed hosts, which have multiple network interfaces.
Iperf in UDP server mode
  Join to a multicast group
  Addresses in the range 224.0.0.0 to 239.255.255.255

## Slide 28: Laboratory 4: Reliable File Transfer
The First Group Project
  Competitively scored
Purpose
  Learn to configure and use DETER
  Collaborative learning
  Understanding through a realistic application
Submission
  Create a document describing the answers
  Submit via Moodle
  Submit system performance results via forum

## Slide 29: Problem: TCP congestion control
Approach: increase transmission rate (congestion window size), probing for usable bandwidth, until loss occurs
  additive increase: increase CongWin by 1 MSS every RTT until loss detected
  multiplicative decrease: cut CongWin in half after loss
congestion window size
Saw tooth
behavior: probing
for bandwidth

## Slide 30: Laboratory 4: Fast and Reliable FTP
Part A
  Each group split into 2 subgroups
    Competing within each group
    Demo both methods on Sept 17th
    Full credit for >20 Mbps on 100Mbps/200ms/20% loss
  Automated script to determine winner
    Extra credit, if your script is used in Part B
  Daily progress must be posted on the forum!
100 Mbps
200ms RTT
20% packet loss

## Slide 31: Laboratory 4: Fast and Reliable FTP
Part B
  Each group merge the best techniques
  Tournament Qualification: >40 Mbps (full credit)
The Tournament
  September 24th: tournament at demo
  September 25th: the finalists compete in class
  The winner(s) will get extra credit
CSCI 558L FTP Tournament

## Slide 32: Next
Next Lecture
  Transport Layer
Laboratory 4: Fast and Reliable FTP
  Part A – Due Sept 15th, demo 17th
  Part B – Demo Sept 24th ,Finalists Compete 25th
Reading Assignment
  Gerla, M. et al, "Generalized Window Advertising for TCP Congestion Control", UCLA Tech Report, Feb 1999.
  Due September 15 at 11:55pm