## Slide 1: CSCI 558L Lecture 7: Routing In Internet
Internetworking and Distributed Systems Laboratory
Young Cho
Department of Computer Science
University of Southern California

## Slide 2: Network and Routers
H3
Destination | Next Hop
H1 | R3
H3 | R3
H4 | R6

## Slide 3: Internet Structure
Original idea
Backbone service provider
Large corporation
Small
corporation
“
Consumer
”
ISP
“
Consumer
”
ISP
“
Consumer
”
ISP
“
Consumer
”
ISP
Small
corporation
Small
corporation
Small
corporation

## Slide 4: Internet Structure
Today
Backbone service provider
Peering
point
Peering
point
Large corporation
Large corporation
Small
corporation
“
Consumer
”
ISP
“
Consumer
”
ISP
“
Consumer
”
ISP

## Slide 5: Route Propagation in the Internet
Autonomous System (AS)
  corresponds to an administrative domain
  examples: University, company, backbone network
  assign each AS a 16-bit number
Two-level route propagation hierarchy
  interior gateway protocol (each AS selects its own)
  exterior gateway protocol (Internet-wide standard)
Routes information is propagated at various levels
  hosts know local router
  local routers know site routers
  site routers know core router
  core routers know everything

## Slide 6: Routing in the Internet
Routing Information Protocol (RIP)
Open Shortest Path First (OSPF)
Border Gateway Protocol (BGP)
Routing Algorithms and Techniques

## Slide 7: Popular Interior Gateway Protocols
RIP: Route Information Protocol
  distributed with BSD Unix
  distance-vector algorithm
  based on hop-count (infinity set to 16)
OSPF: Open Shortest Path First
  recent Internet standard
  uses link-state algorithm
  supports load balancing
  supports authentication

## Slide 8: RIP ( Routing Information Protocol)
distance vector algorithm
included in BSD-UNIX Distribution in 1982
distance metric: # of hops (max = 15 hops)
D
C
B
A
u
v
w
x
y
z
destination hops
u 1
v 2
w 2
x 3
y 3
z 2
From router A to subnets:

## Slide 9: RIP advertisements
Distance Vectors
  Exchanged among neighbors every 30 sec via Response Message (also called advertisement)
Advertisement
  Each lists of up to 25 destination subnets within Autonomous Systems (AS)
  AS - typically an Internet service provider or a very large organization with independent connections to multiple networks, that adhere to a single and clearly defined routing policy

## Slide 10: RIP: Example
Destination Network Next Router Num. of hops to dest.
w A 2
y B 2
z B 7
x -- 1
…. …. ....
Routing/Forwarding table in D
w
x
y
z
A
C
D
B
Dest Next hops
w - 1
x - 1
z C 4
…. … ...
Advertisement
A
5

## Slide 11: RIP Table processing
RIP routing tables managed by application-level process called route-d(aemon)
Advertisements sent in periodic UDP packets
physical
link
network forwarding
(IP) table
Transprt
(UDP)
routed
physical
link
network
(IP)
Transprt
(UDP)
routed
forwarding
table

## Slide 12: RIP: Link Failure and Recovery
If no advertisement heard after 180 sec --> neighbor/link declared dead
Routes via neighbor invalidated
New advertisements sent to neighbors
Neighbors in turn send out new advertisements
  If tables changed
  Link failure info quickly propagates to entire net
poison reverse used to prevent ping-pong loops
  infinite distance = 16 hops – reports dead link

## Slide 13: OSPF (Open Shortest Path First)
“Open”: publicly available
Uses Link State algorithm
  Every node constructs a map of the connectivity to the network
  Each node independently calculates the next best logical hop
  The collection of best next hops form the node's routing table
  Only information passed between nodes is connectivity
Route computation using Dijkstra’s algorithm
  Shortest path for a graph with nonnegative edge path costs
  Produces a shortest path tree
OSPF advertisement carries one entry per neighbor
  Advertisements disseminated to entire AS (via flooding)
  Carried in OSPF messages directly over IP (rather than TCP or UDP)

## Slide 14: Link State Algorithm
Each router maintains a database containing map of the whole topology
  Links
  State (including cost)
All routers have the same information
All routers calculate the best path to every destination
Any link state changes are flooded across the network
"Global spread of local knowledge”

## Slide 15: Link State vs. Distance vector
Distance Vector
  views net topology from neighbor’s perspective
  adds distance vectors from route to router
  frequent, periodic updates; slow convergence
  passes copies of routing table to neighbor routers
Link-State
  gets common view of entire network topology
  calculates the shortest path to other routers
  event-triggered updates; faster convergence
  passes link-state routing updates to other routers

## Slide 16: Distance Vector vs Link State
Distance vector routers compute the best path from information passed to them from neighbors
Link State routers each have a copy of the entire network map
Link State routers compute best routes from this local map

## Slide 17: OSPF “advanced” Features
Security
  all OSPF messages authenticated
  prevents malicious intrusion
Multiple same-cost paths allowed
  contrasts to one path in RIP
Different Type of Service (TOS)
  satellite link cost set
  “low” for best effort
  high for real time
Uni- and multicast support
Hierarchical OSPF in large domains

## Slide 18: Hierarchical OSPF
Two-level hierarchy
  local area, backbone
  LS advertisements only in area
  each nodes has detailed area topology; only know shortest path to nets in other areas.
Area border routers
  “summarize” distances to nets in own area, advertise to other Area Border routers.
Backbone routers
  OSPF routing limited to backbone
Boundary routers
  connect to other AS’s.

## Slide 19: EGP: Exterior Gateway Protocol
Overview
  Original standard for Internet routing protocol (c 1983)
  designed for tree-structured Internet
    Single backbone
  concerned with reachability, not optimal routes
Protocol messages
  neighbor acquisition: one router requests that another be its peer; peers exchange reachability information
  neighbor reachability: one router periodically tests if the another is still reachable; exchange HELLO/ACK messages;
    uses a k-out-of-n rule: ¼ to stay up, ¾ to establish
  routing updates: peers periodically exchange their routing tables (including route weights) using a basic distance vector method
    There can be multiple connections between ASs

## Slide 20: Limits of EGP
At first glance, EGP seems like a distance vector protocol since updates carry lists of destinations and distances – but distances are NOT reliable.
EGP was designed to support tree topologies, not meshes
  False routes injected by accident can have really bad consequences (black holes) – there is no easy way for dealing with this problem
  Loops can easily occur – all we are doing is forwarding routing tables
EGP was not designed to easily support fragmented IP packets – all data is assumed to fit in MTU.
Solutions to these and other EGP problems were all manual

## Slide 21: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol)
  the de facto standard
  BGP-1 developed in 1989 to address problems with EGP.
  Assumes Internet is an arbitrarily interconnected set of ASs
BGP provides each AS a means to:
  Obtain subnet reachability information from neighboring ASs
  Propagate reachability information to all AS-internal routers
  Determine “good” routes to subnets based on reachability information and policy.
Allows subnet to advertise its existence in the Internet

## Slide 22: BGP basics
Difference between BGP and other routing protocols
  An external protocol.
  BGP is only used by ISP's or large private networks that span across the globe.
Pairs of routers exchange routing information
  Over semi-permanent TCP connections: BGP sessions
  BGP sessions need not correspond to physical links.
BGP4
  An enhanced version of BGP with reduced routing table size RFC 1771
IBGP
  used "inside" the confines of its own AS an autonomous system
  works much like a "network neighborhood.“
EBGP
  works the opposite of IBGP
  transports information to other BGP enabled systems
  generally not used within the same AS

## Slide 23: BGP routes & Path attributes
Advertised prefix
  prefix + attributes = “route”
Attributes
  Weight
  Local Preference
  Multi-Exit Discriminator
  Origin
  AS_Path
  Next Hop
  Community
Two important attributes:
  AS-PATH: contains ASs through which prefix advertisement has passed: e.g, AS 67, AS 17
  NEXT-HOP: indicates specific internal-AS router to next-hop AS. (may be multiple links from current AS to next-hop-AS)
When gateway router receives route advertisement, uses import policy to accept/decline.

## Slide 24: BGP route selection
More than 1 route to some prefix
  Router must select route.
Elimination rules
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 25: BGP messages
BGP messages exchanged using TCP.
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 26: Distributing reachability info
Using eBGP session between 3a and 1c
  AS3 sends prefix reachability info to AS1.
  1c can then use iBGP do distribute new prefix info to all routers in AS1
  1b can then re-advertise new reachability info to AS2 over 1b-to-2a eBGP
Router creates entry for the new prefix in its forwarding table
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
eBGP session
iBGP session

## Slide 27: BGP routing policy
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
  X does not want to route from B via X to C
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 28: BGP routing policy (2)
A advertises path AW to B
B advertises path BAW to X
Should B advertise path BAW to C?
  No way! B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
  B wants to force C to route to w via A
  B wants to route only to/from its customers!
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 29: Why different Intra- and Inter-AS routing ?
Policy:
Inter-AS: admin wants control over how its traffic routed, who routes through its net.
Intra-AS: single admin, so no policy decisions needed
Scale:
hierarchical routing saves table size, reduced update traffic
Performance:
Inter-AS: policy may dominate over performance
Intra-AS: can focus on performance

## Slide 30: Other Routing Algorithms
Many Techniques
  Described at the end for you to review
Interesting Details
  But not the focus of the course

## Slide 31: Next
Next Lecture
  Details of IP
Laboratory
  Fast and Reliable File Transfer Tournament
  Use the script
  The Tournament Sept 24
  Semi-final/Final on Sept 25 in class
  Final Source Code due Sept 25 at 11:55pm
Reading Assignment
  White, L. et al, "An Integrated Experimental Environment for Distributed Systems and Networks", OSDI 2002, December 2002.

## Slide 32: Other Routing Algorithms

## Slide 33: Broadcast Routing
deliver packets from source to all other nodes
source duplication is inefficient:
R1
R2
R3
R4
source duplication
R1
R2
R3
R4
in-network
duplication
duplicate
creation/transmission
duplicate
duplicate
source duplication
  how does source determine recipient addresses?

## Slide 34: In-network duplication
flooding: when node receives brdcst pckt, sends copy to all neighbors
  Problems: cycles & broadcast storm
controlled flooding: node only brdcsts pkt if it hasn’t brdcst same packet before
  Node keeps track of pckt ids already brdcsted
  Or reverse path forwarding (RPF): only forward pckt if it arrived on shortest path between node and source
spanning tree
  No redundant packets received by any node

## Slide 35: Spanning Tree
First construct a spanning tree
Nodes forward copies only along spanning tree
A
B
G
D
E
c
F
A
B
G
D
E
c
F
(a) Broadcast initiated at A
(b) Broadcast initiated at D

## Slide 36: Spanning Tree: Creation
Center node
Each node sends unicast join message to center node
  Message forwarded until it arrives at a node already belonging to spanning tree
A
B
G
D
E
c
F
1
2
3
4
5
Stepwise construction of spanning tree
A
B
G
D
E
c
F
(b) Constructed spanning tree

## Slide 37: Multicast Routing
Goal: find a tree (or trees) connecting routers having local mcast group members
  tree: not all paths between routers used
  source-based: different tree from each sender to rcvrs
  shared-tree: same tree used by all group members
Shared tree
Source-based trees
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-9

## Slide 38: Approaches for building mcast trees
Approaches:
source-based tree: one tree per source
  shortest path trees
  reverse path forwarding
group-shared tree: group uses one tree
  minimal spanning (Steiner)
  center-based trees
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-11

## Slide 39: Shortest Path Tree
mcast forwarding tree: tree of shortest path routes from source to all receivers
  Dijkstra’s algorithm
R1
R2
R3
R4
R5
R6
R7
2
1
6
3
4
5
i
router with attached
group member
router with no attached
group member
link used for forwarding,
i indicates order link
added by algorithm
LEGEND
S: source
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-12

## Slide 40: Reverse Path Forwarding
if (mcast datagram received on incoming link on shortest path back to center)
then flood datagram onto all outgoing links
else ignore datagram
rely on router’s knowledge of unicast shortest path from it to sender
each router has simple forwarding behavior:
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-13

## Slide 41: Reverse Path Forwarding: example
result is a source-specific reverse SPT
  may be a bad choice with asymmetric links
R1
R2
R3
R4
R5
R6
R7
router with attached
group member
router with no attached
group member
datagram will be forwarded
LEGEND
S: source
datagram will not be
forwarded
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-14

## Slide 42: Reverse Path Forwarding: pruning
forwarding tree contains subtrees with no mcast group members
  no need to forward datagrams down subtree
  “prune” msgs sent upstream by router with no downstream group members
R1
R2
R3
R4
R5
R6
R7
router with attached
group member
router with no attached
group member
prune message
LEGEND
S: source
links with multicast
forwarding
P
P
P
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-15

## Slide 43: Shared-Tree: Steiner Tree
Steiner Tree: minimum cost tree connecting all routers with attached group members
problem is NP-complete
excellent heuristics exists
not used in practice:
  computational complexity
  information about entire network needed
  monolithic: rerun whenever a router needs to join/leave
Notes: Notes:
1. See L. Wei and D. Estrin, “A Comparison of multicast trees and algorithms,” TR USC-CD-93-560, Dept. Computer Science, University of California, Sept 1993 for a comparison of heuristic approaches.
3.3 Network Layer: Multicast Routing Algorithms 3-16

## Slide 44: Center-based trees
single delivery tree shared by all
one router identified as “center” of tree
to join:
  edge router sends unicast join-msg addressed to center router
  join-msg “processed” by intermediate routers and forwarded towards center
  join-msg either hits existing tree branch for this center, or arrives at center
  path taken by join-msg becomes new branch of tree for this router
Notes: Notes:
1. It’s always nice to see a PhD dissertation with impact. The earliest discussion of center-based trees for multicast appears to be D. Wall, “Mechanisms for Broadcast and Selective Broadcast,” PhD dissertation, Stanford U., June 1980.
3.3 Network Layer: Multicast Routing Algorithms 3-17

## Slide 45: Center-based trees: an example
Suppose R6 chosen as center:
R1
R2
R3
R4
R5
R6
R7
router with attached
group member
router with no attached
group member
path order in which join messages generated
LEGEND
2
1
3
1
Notes: Notes:
3.3 Network Layer: Multicast Routing Algorithms 3-18

## Slide 46: Internet Multicasting Routing: DVMRP
DVMRP: distance vector multicast routing protocol, RFC1075
flood and prune: reverse path forwarding, source-based tree
  RPF tree based on DVMRP’s own routing tables constructed by communicating DVMRP routers
  no assumptions about underlying unicast
  initial datagram to mcast group flooded everywhere via RPF
  routers not wanting group: send upstream prune msgs
Notes: Notes:
D. Waitzman, S. Deering, C. Partridge, “Distance Vector Multicast Routing Protocol,” RFC 1075, Nov. 1988. The version of DVMRP in use today is considerably enhanced over the RFC1075 spec.
A more up-to-date “work-in-progress” defines a version 3 of DVMRP: T. Pusateri, “Distance Vector Multicast Routing Protocol,” work-in-progress, draft-ietf-idmr-v3-05.ps
3.4 Network Layer: Internet Multicast Routing Algorithms 3-20

## Slide 47: DVMRP: continued…
soft state: DVMRP router periodically (1 min.) “forgets” branches are pruned:
  mcast data again flows down unpruned branch
  downstream router: reprune or else continue to receive data
routers can quickly regraft to tree
  following IGMP join at leaf
odds and ends
  commonly implemented in commercial routers
  Mbone routing done using DVMRP
Notes: Notes:
1. See www.mbone.com/mbone/routers.html for a (slightly outdatet) list of multicast capable routers (supporting DVMPR as well as other protocols) from various vendors.
2. ftp://parcftp.xerox.com/pub/net-research/ipmulti for circa 1996 public copy “mrouted” v3.8 of DVMRP routing software for various workstation routing platforms.
3.4 Network Layer: Internet Multicast Routing Algorithms 3-21

## Slide 48: Tunneling
Q: How to connect “islands” of multicast routers in a “sea” of unicast routers?
mcast datagram encapsulated inside “normal” (non-multicast-addressed) datagram
normal IP datagram sent thru “tunnel” via regular IP unicast to receiving mcast router
receiving mcast router unencapsulates to get mcast datagram
physical topology
logical topology
Notes: Notes:
For a general discussion of IP encapsulation, see C. Perkins, “IP Encapsulation within IP,” RFC 2003, Oct. 1996.
The book S. Bradner, A Mankin, “Ipng: Internet protocol next generation,” Addison Wesley, 1995 has a very nice discussion of tunneling
Tunneling can also be used to connect islands of IPv6 capable routers in a sea IPv4 capable routers. The long term hope is that the sea evaporates leaving only lands of IPv6!
3.4 Network Layer: Internet Multicast Routing Algorithms 3-22

## Slide 49: Protocol Independent Multicast
not dependent on any specific underlying unicast routing algorithm (works with all)
two different multicast distribution scenarios :
Dense:
group members densely packed, in “close” proximity.
bandwidth more plentiful
Sparse:
# networks with group members small wrt # interconnected networks
group members “widely dispersed”
bandwidth not plentiful
Notes: Notes:
a very readable discussion of the PIM architecture is S. Deering, D. Estrin, D. Faranacci, V. Jacobson, C. Liu, L. Wei, “The PIM Architecture for Wide Area Multicasting,” IEEE/ACM Transactions on Networking, Vol. 4, No. 2, April 1996.
D. Estrin et al, PIM-SM: Protocol Specification, RFC 2117, June 1997
S. Deering et al, PIM Version 2, Dense Mode Specification, work in progress, draft-ietf-idmr-pim-dm-05.txt
PIM is implemented in Cisco routers and has been deployed in UUnet as part of their streaming multimedia delivery effort. See S. LaPolla, “IP Multicast makes headway among ISPs,” PC Week On-Line, http://www.zdnet.com/pcweek/news/1006/06isp.html
3.4 Network Layer: Internet Multicast Routing Algorithms 3-25

## Slide 50: Consequences of Sparse-Dense Dichotomy:
Dense
group membership by routers assumed until routers explicitly prune
data-driven construction on mcast tree (e.g., RPF)
bandwidth and non-group-router processing profligate
Sparse:
no membership until routers explicitly join
receiver- driven construction of mcast tree (e.g., center-based)
bandwidth and non-group-router processing conservative
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-26

## Slide 51: PIM- Dense Mode
flood-and-prune RPF, similar to DVMRP but
  underlying unicast protocol provides RPF info for incoming datagram
  less complicated (less efficient) downstream flood than DVMRP reduces reliance on underlying routing algorithm
  has protocol mechanism for router to detect it is a leaf-node router
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-27

## Slide 52: PIM - Sparse Mode
center-based approach
router sends join msg to rendezvous point (RP)
  intermediate routers update state and forward join
after joining via RP, router can switch to source-specific tree
  increased performance: less concentration, shorter paths
R1
R2
R3
R4
R5
R6
R7
join
join
join
all data multicast
from rendezvous
point
rendezvous
point
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-28

## Slide 53: PIM - Sparse Mode
sender(s):
unicast data to RP, which distributes down RP-rooted tree
RP can extend mcast tree upstream to source
RP can send stop msg if no attached receivers
  “no one is listening!”
R1
R2
R3
R4
R5
R6
R7
join
join
join
all data multicast
from rendezvous
point
rendezvous
point
Notes: Notes:
3.4 Network Layer: Internet Multicast Routing Algorithms 3-29